## Slide 1
Chapter 1 Introduction
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Notes: Version History
7.2 (January 2020)
All slides reformatted for 16:9 aspect ratio
Use of Calibri font, rather that Gill Sans MT
Updated slide content for 2020 link technologies and applications
Add more animation throughout
New Master slide
Feb. 2020
a few updates suggest by Catherine Rosenberg (thanks!)
titles in a lighter font

## Slide 2: Chapter 1: introduction
Chapter goal:
Get “feel,” “big picture,” introduction to terminology
  more depth, detail later in course
Approach:
  use Internet as example
Overview/roadmap:
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 3: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 4: “Fun” Internet-connected devices
IP picture frame
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: remote
control cable TV
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Security Camera
Amazon Echo
Pacemaker & Monitor
Others?
Fitbit
AR devices

## Slide 5: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video

## Slide 6: The Internet: a “service” view
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 7: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when message received, or other events
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 8: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 9: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 10: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers

## Slide 11: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 12: A closer look at Internet structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 13: Access networks and physical media
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks (WiFi, 4G/5G)
What to look for:
transmission rate (bits per second) of access network?
shared or dedicated access among users?

## Slide 14: Access networks: cable-based access
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing (FDM): different channels transmitted in different frequency bands

## Slide 15: Access networks: cable-based access
cable
modem
splitter
…
cable headend
data, TV transmitted at different
frequencies over shared cable
distribution network
HFC: hybrid fiber coax
  asymmetric: up to 40 Mbps – 1.2 Gbs downstream transmission rate, 30-100 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
cable modem
termination system
CMTS
ISP

## Slide 16: Access networks: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  24-52 Mbps dedicated downstream transmission rate
  3.5-16 Mbps dedicated upstream transmission rate
DSL
modem
splitter
DSL access
multiplexer

## Slide 17: Access networks: home networks
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
WiFi wireless access
point (54, 450 Mbps)
wireless
devices
often combined
in single box

## Slide 18: Wireless access networks
Shared wireless access network connects end system to router
via base station aka “access point”
Wireless local area networks (WLANs)
  typically within or around building (~100 ft)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
to Internet
to Internet
Wide-area cellular access networks
  provided by mobile, cellular network operator (10’s km)
  10’s Mbps
  4G cellular networks (5G coming)

## Slide 19: Access networks: enterprise networks
companies, universities, etc.
  mix of wired, wireless link technologies, connecting a mix of switches and routers (we’ll cover differences shortly)
    Ethernet: wired access at 100Mbps, 1Gbps, 10Gbps
    WiFi: wireless access points at 11, 54, 450 Mbps
Ethernet
switch
institutional mail,
web servers
institutional router
Enterprise link to
ISP (Internet)

## Slide 20: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 21: Links: physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet

## Slide 22: Links: physical media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 23: Links: physical media
Wireless radio
signal carried in electromagnetic spectrum
no physical “wire”
broadcast and “half-duplex” (sender to receiver)
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  up to 45 Mbps channels
Wireless LAN (WiFi)
  Up to 100’s Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10’s Mbps
satellite
  up to 45 Mbps per channel
  270 msec end-end delay
  geosynchronous versus low-earth-orbit

## Slide 24: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 25: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 26: Packet-switching: store-and-forward
Transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
Store and forward: entire packet must arrive at router before it can be transmitted on next link
End-end delay: 2L/R (above), assuming zero propagation delay (more on delay shortly)
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 27: Packet-switching: queueing delay, loss
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for a period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link

## Slide 28: Two key network-core functions
Forwarding:
local action: move arriving packets from router’s input link to appropriate router output link
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
local forwarding table
local forwarding table
routing algorithm

## Slide 29: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 30: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
each call allocated its own band, can transmit at max rate of that narrow band
Time Division Multiplexing (TDM)
time divided into slots
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band, but only during its time slot(s)

## Slide 31: Packet switching versus circuit switching
Example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
packet switching allows more users to use network!
N
users
1 Gbps link
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
circuit-switching: 10 users
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
packet switching: with 35 users, probability > 10 active at same time is less than .0004 *
Notes: Slide #31, Chapter 1:
nCr: the number of combinations of n things, taken r at a time.
nCr = (n!) / [x!(n-x)!]
35C11 = 35! / [(11!)(24!)] = 417,225,900
Binomial probability = p = b(x; n, P) = nCx * Px * (1 - P)n – x or b(x; n, P) = { n! / [ x! (n - x)! ] } * Px * (1 - P)n – x

## Slide 32: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees traditionally used for audio/video applications
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?

## Slide 33: Internet structure: a “network of networks”
Hosts connect to Internet via access Internet Service Providers (ISPs)
    residential, enterprise (company, university, commercial) ISPs
Access ISPs in turn must be interconnected
    so that any two hosts can send packets to each other
Resulting network of networks is very complex
    evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 34: Internet structure: a “network of networks”
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 35: Internet structure: a “network of networks”
…
…
…
…
…
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 36: Internet structure: a “network of networks”
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 37: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….

## Slide 38: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. who will want to be connected
IXP
peering link
Internet exchange point
IXP

## Slide 39: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
IXP
IXP
access
net
access
net
regional ISP
access
net
access
net
access
net

## Slide 40: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP

## Slide 41: Internet structure: a “network of networks”
Tier 1 ISP
Tier 1 ISP
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
IXP
IXP
IXP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Google

## Slide 42: Tier-1 ISP Network map: Sprint (2019)
links to/from Sprint customer networks
links to peering networks
to/from other Sprint PoPS
…
…
…
…
…
POP: point-of-presence

## Slide 43: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 44: How do packet loss and delay occur?
packets queue in router buffers
packets queue, wait for turn
arrival rate to link (temporarily) exceeds output link capacity: packet loss
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 45: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop
propagation
nodal
processing
queueing
A
B
transmission

## Slide 46: Packet delay: four sources
dnodal = dproc + dqueue + dtrans + dprop
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
* Check out the online interactive exercises: http://gaia.cs.umass.edu/kurose_ross
propagation
nodal
processing
queueing
A
B
transmission

## Slide 47: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km

## Slide 48: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 49: Packet queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
La/R ~ 0: avg. queueing delay small
La/R <= 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
Notes: Example traffic intensity:
R 100000 bits/s
L 2000 bits per packet
a 50 packets per sec
La 100000 bits per second
La/R 1 Traffic Intensity

## Slide 50: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply
Notes: NOTE: Use ‘tracert’ in Windows.
ICMP echo messages may be rejected/disabled by most routers.

## Slide 51: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link
* Do some traceroutes from exotic countries at www.traceroute.org
looks like delays decrease! Why?
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu

## Slide 52: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 53: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 54: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
Notes: The server pumps water at a rate of Rs or lower.
The throughput = min(Rc, Rs). //That is, the rate of the ‘bottleneck link’

## Slide 55: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 56: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History
Notes: Segue: from performanceto security

## Slide 57: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 58: Bad guys: malware
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam or distributed denial of service (DDoS) attacks
Notes: “A worm can replicate and spread itself from one computer to another. On the other hand, a virus cannot self-replicate, and it needs to be sent by a user or software to travel between two different computers.” (https://www.fortinet.com/resources/cyberglossary/malware-vs-virus-vs-worm#:~:text=A%20worm%20can%20replicate%20and,travel%20between%20two%20different%20computers.)

## Slide 59: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 60: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for our end-of-chapter labs is a (free) packet-sniffer

## Slide 61: Bad guys: fake identity
IP spoofing: send packet with false source address
A
B
C
… lots more on security (throughout, Chapter 8)
src:B dest:A payload

## Slide 62: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 63: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 64: Example: organization of air travel
airline travel: a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 65: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Q: describe in words the service provided in each layer above

## Slide 66: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?
layering in other complex systems?
Notes: “ One potential drawback of layering is that one layer may duplicate lower-layer functionality.
For example, many protocol stacks provide error recovery on both a per-link basis and an end-to-end basis.
* A second potential drawback is that functionality at one layer may need information (for example, a timestamp value) that is present only in another layer; this violates the goal of separation of layers.

## Slide 67: Internet protocol stack
application: supporting network applications
  IMAP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
Notes: “IMAP, or Internet Message Access Protocol, is a protocol that allows email clients to retrieve messages from a mail server.”
“IMAP, or Internet Message Access Protocol, is a protocol that allows email clients to retrieve messages from a mail server.”

## Slide 68: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 69: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 70: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 71: Internet history
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
1972-1980: Internetworking, new and proprietary nets
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best-effort service model
  stateless routing
  decentralized control
define today’s Internet architecture

## Slide 72: Internet history
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 73: Internet history
early 1990s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990s: commercialization of the Web
late 1990s – 2000s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000s: commercialization, the Web, new applications

## Slide 74: Internet history
~18B devices attached to Internet (2017)
    rise of smartphones (iPhone: 2007)
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access: 4G/5G, WiFi
emergence of online social networks:
  Facebook: ~ 2.5 billion users
service providers (Google, FB, Microsoft) create their own networks
    bypass commercial Internet to connect “close” to end user, providing “instantaneous” access to search, video content, …
enterprises run their services in “cloud” (e.g., Amazon Web Services, Microsoft Azure)
2005-present: more new applications, Internet is “everywhere”

## Slide 75: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 76: Additional Chapter 1 slides

## Slide 77: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model

## Slide 78: Wireshark
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received